MODBUS FRAMES:-

Modbus is a data communications protocol originally published by Modicon (now Schneider Electric) in 1979 for use with its programmable logic controllers (PLCs). Modbus has become a de facto standard communication protocol and is now a commonly available means of connecting industrial electronic devices

- Modbus is popular in industrial environments because it is openly published and royalty-free. It was developed for industrial applications, is relatively easy to deploy and maintain compared to other standards, and places few restrictions on the format of the data to be transmitted.
- The Modbus protocol uses character serial communication lines, Ethernet, or the Internet protocol suite as a transport layer. Modbus supports communication to and from multiple devices connected to the same cable or Ethernet network.
- For example, there can be a device that measures temperature and another device to measure humidity connected to the same cable, both communicating measurements to the same computer, via Modbus
- Modbus is often used to connect a plant/system supervisory computer with a remote terminal unit (RTU) in supervisory control and data acquisition (SCADA) systems.
- Many of the data types are named from industrial control of factory devices, such as ladder logic because of its use in driving relays: a single-bit physical output is called a coil, and a single-bit physical input is called a discrete input or a contact.
MODBUS OBJECT TYPES:-
The following object types may be provided by a Modbus server to a Modbus client device:[7] The addresses are representative of the original Modicon specification. Under the current standard the address can be 0 - 65535 with the object type identified by the command used to read or write the coil or register.